## Slide 1: Packet Queuing & Scheduling
Asima Nisar
PhD - CS candidate
(Communication & Networks)

## Slide 2: Agenda
Packet Queuing Vs. Cellification
Packet Queuing & Scheduling: Need
Packet Queuing & Scheduling: Why?
Packet Queuing & Scheduling: Most Important Parameters
Packet Queuing & Scheduling mechanisms: Objective
Packet Queuing & Scheduling mechanisms: Types
FQ: Fair Queuing mechanism
FQ mechanism: Issue
FQ mechanism: Limitations
WFQ: Weighted Fair Queuing mechanism
WFQ: Advantage & Drawback
WFQ: Benefits
WFQ: Limitations
References
Qs & As

## Slide 3: Packet Queuing Vs. Cellification
Routers can handle packet queuing in two different ways, either queuing the entire packet or splitting it into fixed size cells, a process commonly called cellification [2].
Queuing the entire packet is the older method and is conceptually simpler. It is commonly used in CPU processing-based forwarding routers. In this scenario, there is no split between the control and forwarding planes, which typically does not become a limiting factor if the supported interfaces are low- speed ones [2].

## Slide 4: Packet Queuing Vs. Cellification
However, queuing the entire packet has its drawbacks, which have led to the appearance and popularity of cellification. A packet has a variable length, so different packet lengths imply different processing delays [2].
The cellification process chops a packet into fixed-sized cells, which makes it easier for the router’s memory management to deal with the packets. It also provides consistency in terms of transmission times and slots for the buffering required [2].

## Slide 5: Packet Queuing & Scheduling: Need
Selection of proper packet scheduling algorithm is crucial component in QoS provisioning over next generation networks, especially when higher throughput with better QoE (Quality of Experience) is expected among the users [1].

## Slide 6: Packet Queuing & Scheduling: Why?
Queuing and scheduling mechanisms allow traffic to be split into multiple queues so that the scheduler can decide which type of treatment the traffic inside each queue receives [2].

## Slide 7: Packet Queuing & Scheduling: Most Important Parameters
The two most important parameters associated with the queuing and scheduling mechanisms are [2]:
Buffers
Bandwidth
Buffering is the length of the queue, i.e. how much memory is available to store packets [2].
Bandwidth is the amount of data that can be transmitted in a fixed amount of time [4].
For digital devices: Bandwidth is expressed as bit/sec or byte/sec.
For analog devices: Bandwidth is expressed as cycle/sec or Hertz.

## Slide 8: Packet Queuing & Scheduling mechanisms: Objective
The queuing and scheduling discipline used determines how the resources are allocated. The requirement for the presence of queuing and scheduling is typically controlled by the presence of congestion. If resources are sufficient and there is no competition for resources, there is no need for queuing [2].
NB: A packet enters a queue at the tail, remains in the queue until it reaches the head, and then leaves the queue. In a queuing system, packets can be dropped from either the tail or the head of the queue, and can even be dropped from both at the same time. Most commonly, packets are dropped from the tail [2].

## Slide 9: Packet Queuing & Scheduling mechanisms: Types
Some major well-known disciplines regarding scheduling are listed here [2]:
• First in, first out (FIFO) queuing
• Fair queuing (FQ)
• Priority queuing (PQ)
• Weighted fair queuing (WFQ)
• Weighted round robin (WRR)
• Deficit weighted round robin (DWRR)
• Priority-based deficit weighted round robin (PB-DWRR)

## Slide 10: FQ: Fair Queuing mechanism
FQ, defined by Nagle in 1985, takes into account packet size to ensure that each flow receives an equal opportunity to transmit an equal amount of data [2].
Each queue is assigned the same weight; that is, the queues are scheduled with the same amount of bandwidth [2].
This scheme avoids the problems of dealing with small and large packets in the queue, so the speed of removal from the queue is a function of a number of bits, not a function of a number of packets [2].

## Slide 11: FQ: Fair Queuing mechanism: Issue
The main issue with the fairness algorithm is the fact that it is indeed fair, which may seem odd but it does invalidate the desired QoS goal of providing an uneven distribution of resources across different classes of service. If many queues must be visited in a fair order, flows that require low delay can suffer [2].

## Slide 12: FQ: Fair Queuing mechanism: Limitations
FQ has the following limitations [2]:
• The FQ algorithm is extremely complicated to implement. So, FQ is more of a theoretical construct than a practical paradigm.
• It is resource-intensive because many states and hashes must be computed and because memory must be allocated and reallocated based on changes in the session state.
• Delay and jitter can still be issues because each session hash is seen as a queue entity. The wait time to the next scheduled service can be long if many sessions are active.

## Slide 13: WFQ: Weighted Fair Queuing mechanism
WFQ was developed in 1989 by Demers, Keshav, Shenke, and Zhang, and emulates the Generic Processor Sharing (GPS) concepts of virtual processing time [3].
Weighted fair queuing (WFQ) is commonly referred as "bit-by-bit round robin," because it implements a queuing and scheduling mechanism in which the queue servicing is based on bits instead of packets [3].
In WFQ, each queue or flow is allocated a weight that is a proportion of the interface rate or the shaping rate [3].
With WFQ, each queue is scheduled based on a computation performed on the bits of each packet at the head of the queue. Because the traffic computation is done based on stream of bits and not of packets, and because what the router receives and transmits are indeed packets, WFQ implicitly increases complexity [3].

## Slide 14: WFQ: Weighted Fair Queuing: Advantage & Drawback
WFQ is aware of packet sizes and can thus support variable-sized packets. The benefit is that sessions with big packets do not get more scheduling time than sessions with smaller packets, because effectively the focus of WFQ is bits and not packets. So there is no unfairness in the scheduling for sessions with smaller packet sizes [3].
The drawback of WFQ is that it is very resource-intensive because of the bit computations. The original WFQ idea also consumes many resources because the flows are not aggregated into classes with limited queues. Instead, each flow or stream gets its own queue or buffer quota, similar to FQ. Because of these high resource demands and the complex computation needed to check the state for each flow and its packets, WFQ has been implemented more on CPU-based platforms whose queuing disciplines are based on bus-based architectures [3].

## Slide 15: WFQ: Weighted Fair Queuing: Benefits
WFQ has the following benefits:
The implementations based on WFQ algorithm provide service differentiation between classes and their aggregated traffic, rather than merely differentiating between individual flows [3].
A weight allocated to each class divides the scheduling and bandwidth ratio for each class [3].
Also, because WFQ is bits aware, it can handle packets of variable lengths [3].

## Slide 16: WFQ: Weighted Fair Queuing: Limitations
WFQ has the following limitations:
• The original WFQ design is more of a queuing theory. The existing implementations do not follow the original concept in which each flow is allocated a weight. Instead, flows are aggregated by being classified into different service classes, and these classes are then assigned to queues [3].
• WFQ is extremely complicated to implement, as is FQ. Maintaining state information and computing the hash table are resource – intensive tasks [3].

## Slide 17: References
https://www.ijser.org/researchpaper/Packet-scheduling-in-LTE-mobile-network.pdf
http://what-when-how.com/qos-enabled-networks/queuing-and-scheduling-qos-enabled-networks-part-1/
http://what-when-how.com/qos-enabled-networks/queuing-and-scheduling-qos-enabled-networks-part-2/
https://www.webopedia.com/TERM/B/bandwidth.html

## Slide 18
Question(s) & Answer(s)
THANK YOU..